## Slide 1: Introduction & Passive Components
Intro to DIY Circuit Design
Zhiyang Tsao
Summer 2024

## Slide 2
About me
陈 悦开 / Pieski
Electronic Information Engineering,
College of EE, Zhejiang Univ.
Power Electronics
Nothing else, actually
E-mail: tsaozy@zju.edu.cn / tinesharp@outlook.com (after graduation)
Github: https://github.com/Pieski
Wechat: “脑子有坑”in every xlab wechat group

## Slide 3
About this program
A brief introduction to the basic electronic engineering
Multiple DIY-level designs
A tutorial of design and simulation tools
A little bit math

## Slide 4
On what level do we design?
Embedded System
“Software”
Too soft
Too hard
Hardware
Physics, electro-chemistry
System Level
Product
Too big
Too specific
Circuit Level
IC design
Semiconductor
Module
Device on sale
Too easy
Too hard
PCBA
Discrete transistors
Fricking vacuum tubes

## Slide 5
Example: Power Supply
1kW Bidirectional Isolated DC/DC Converter
2024

## Slide 6
Example: Embedded Hardware
AR-Track
2024 bwg
PCBs
https://github.com/AAAAyl0n/AR-Track

## Slide 7
Example: Crazy Ideas
60kV 100W Xray
2022

## Slide 8
Passive Components
Passive = It only receives energy / it needs no auxiliary supply /
it is incapable of power gain
Resistor
电阻
Capacitor
电容
Inductor
电感
Antenna
天线

## Slide 9
Resistor
What else?
Always beware of power dissipation!
R0201
P<0.05W
The higher the loss, the larger the size.
Otherwise raised temeperature would damage the resistor irreversible.
Tubular Ceramic Resistor
瓷管电阻，50W~1kW
Resistive Load Bank
负载箱子, ~100kW
Fan

## Slide 10
Calculation!
Suppose we have a CMOS sensor that requires some 1.25V reference voltage.
But I only got a 5V supply. What to do?
For this moment that menas it needs roughly no current.
A basic resistive voltage divider
It only tells us the ratio!
At XLAB we prefer 0805 resistor
For R0805, P<1/8W

## Slide 11
Easier approach
At XLAB we prefer 0805 resistor
For R0805, P<1/8W
永铭 prefers 0603 resistor
P<1/10W
In future you might need R0201
P<1/20W
Approach for the lazy is to start with 10KΩ. It works for most scenarios.
Unaccepctable
Harmless
Beware that 2.5mW is still too high
for certain μW-level ultra low power
applications.
Worth attention
Sometimes you have to compromise
between loss and speed

## Slide 12
More calculation
This chart is plotted for large LEDs!
Suppose we want a red LED works on
Vf = 2.0V & If = 40mA

## Slide 13
How do we actually drives (a lot of) LEDs?
1. PWM
2. CCR
With PWM techniques, luminous flux of LED can be reduced to less than 40% while remaining consistent color.
It a little bit complex, though.
NOTE: LED dimming is a suggested DIY project for this summer

## Slide 14
Capacitor 电容
It is defined as:
Charge quality 电荷量
Voltage
For any component we are interested in its I-V characteristic
But we only got voltage here.
Recap: how is current defined?
Charge flows through some area within
an element of time
Assume that C is time-constant
Current flows through a capacitor is proportional to
The derivative of voltage over time / the voltage changing rate

## Slide 15
Plug a capacitor in DC supply
Boundary conditions, BCs

## Slide 16
Plug a capacitor in AC supply
Transient State
Steady State
Still stands, But V1 is now
You may solve the ODE function, but it is really desperating when the circuit got complicated
In most cases we only care about the steady state, and there are easy tools to solve it.

## Slide 17
Conclude the capacitor in a nut shell
隔直通交
Forget about R1,
We may define a property Reactance in letter X, just like the resistance
The higher the frequency, the lower the reactance of a capacitor.
You may consider it as a frequency-dependent resistor.
When f=0 (DC condition) and in steady state, Xc->∞. In other words it blocks DC current.
When f->∞ (high freq condition) and in ss, Xc->0. It conducts AC current.

## Slide 18
One application: Filter
Recoder
A composition of sine wave
of 1k, 5k and 7kHz
A 20kHz noise

## Slide 19
0.1uF + 10uF
Filter capacitors
Where is the resistor in the RC filter?